draft-ietf-roll-rpl-observations
- ROLL Working Group
IETF 106, Singapore

---
What is this about?
- Aim is to stabilize-fix-clarify RFC 6550
- RFC 6550 observations over period of time
  - Implementation observations
  - Clarify unclear/complex mechanisms in 6550
  - Extracts from mailing list discussions
- Draft keeps record of all the observations

---
Parent Switching
- DTSN
  - Destination Advertisement Trigger Sequence Number
  - Sent in DIO by a parent to trigger DAO from child nodes
- Scenario: Node D switches to parent C
- Very easy to handle in non-storing MOP
  - Only root can increment DTSN

---
Parent Switching – Storing MOP
- Storing MOP, not so easy!
- Two strategies possible
  - Increment DTSN
    - Node D increment DTSN and reset DIO trickle
    - Child nodes of D also reset DIO trickle when they see their preferred parent
    - Thus the whole sub-DODAG rooted at D has resetted their trickle timer.
    - Too bad for control overhead
  - Send aggregated DAO on behalf of sub-DODAG
    - Multiple targets with multiple Transit Info options
    - Single DAO may not fit all targets
      - Splitting across DAOs not an easy thing to handle

---
DAO-ACK handling
- DAO-ACK helps node to ascertain that end to end path is established
  - Indication to start application traffic
- Non-storing MOP
  - DAO sender knows whether root has rcvd the DAO based on DAO-ACK

---
DAO-ACK, Storing MOP
- DAO-ACK sent hop-by-hop
  - Upstream node sending +ve DAO-ACK accepts responsibility to deliver DAO upstream
- Issue
  - Node B responds with DAO-ACK instantly
    - DAO-ACK cannot be used as an indication to start app-traffic
  - What happens if DAO-ACK with -ve status is responded somewhere up?
    - How to inform downstream peer that DAO-ACK failed somewhere upstream?

---
Another DAO-ACK interpretation
- Respond with DAO-ACK only when the peer upstream has ACKed
- Works well for app-traffic start indication
- Problems
  - Routing table needs additional state, thus costly
  - Implementations using different schemes can’t interoperate

---
Design goals for DAO-ACK
- Status=0 as an indication that path is established
- No explicit state should be required on intermediate 6LRs for DAO-ACKing
- DAO-ACK aggregation

---
Signaling Resource Contraints
- Handling resource constraints at multihop
- Need new OCPs to take into account
  - Routing table size
  - Neighbor cache size
- Enrollment priority
  - Step in that direction
  - But needs to be usable at multiple hops

---
Transit Information Option
- TIO design goal
  - Map one or more transit info to one or more targets
  - Provide syntax for aggregating common transit information
- But contains elements which mostly varies on per target
  - E (External):Not a transit info; applies to target
  - E.g. PathSequence and PathLifetime
  - Making it difficult to aggregate efficiently
- TIO is optional as per 6550
  - How should a 6LR/root deal with this?
    - Non-storing mode, parent address is needed
    - Can 6LR assume Path lifetime of 0xff if TIO not present?

---
Eliding Options
- RFC 6550 allows eliding config option
  - But does not give details
  - In its current state, eliding may not work under certain conditions
- We need
  - Eliding to work for Config Option and other static options which rarely change
  - Should be extensible for new options in the future

---
RPL Persistent state
- RPL uses lollipop counters
  - For most of the sequence counters
  - Handling conditions when the node reboots in linear part still requires use of persistent storage
- Inference
  - Lollipop counters reduce the use of persistent storage in circular part but does not fully eliminate the need for it.
Sequence Win = 16 (Def RFC6550)

---
Path Control bits
- What is it?
  - Enables multiple downwards routes
  - Can advertise pref for paths
- Value of Path Control
  - Provides multi-path routing capability
  - Allows traffic load-balancing within a DODAG

---
Path Control Bits
- Not an easy mechanism to implement
  - Impacts Memory and Program size
  - But might be useful in the context of 6tisch/RAW!
- No implementation we know is compliant with the use of Path Control Bits
  - Section 9.9 Point 9 says, “A node MUST NOT unicast a DAO msg that has no active bits in the Path Control field set”.
  - By default, even with one parent at-least a single PC bit must be set
    - Default PCS is 0, which means PCS+1 bit in TIO-PC is in use
  - No implementation handles path-control bits even though 6550 mandates it

---
Miscellaneous
- Mandating support for reception of aggregated targets
- It is possible that DAO-ACK may not be sent even in case the ‘K’ flag (indicating ACK needed) is set.
  - Why is DAO-ACK sending a SHOULD in 6550 even if K flag is set?
- Multi-DODAG/Multi-Instance
  - Should the routing table be reset when switching from one DODAG to another in the same instance?
  - Best practices when handling multi-instance/multi-DODAG
- Why is Transit Information Option optional?
- Is it better to have an RPL-lite with very specific features?
  - No Path Control
  - Support for handling of aggregated targets

---
Overall Status
Point	Status	Remarks
DTSN handling in storing MOP	No update	BCP needed
DAO-ACK	No update	Some work is initiated. Prototype + draft (Rabi?)
Capability & MOPex	draft-ietf-roll-mopex-cap	Draft in-progress
Eliding static info	draft-thubert-roll-eliding-dio-information	Draft in-progress
Miscellaneous	No update	Aggregated Targets handling, TIO vs Target bits
Lollipop Counters	Get WG consensus	Linear part needs to be backed in persistent storage
Resource constraints	No update

---
Other points still uncovered
- Multi-Sink/BR practices
- Multicast Operation
- Partial dependency on ND
  - Prefix Info sent in DIO
  - But Context Table and other global configuration uses ND